## Slide 1
Lecture 4a
Mobile IP
1

## Slide 2: Outline
2
How to support Internet mobility?
– by Mobile IP.
Our discussion will be based on IPv4 (the current version).

## Slide 3: IP Address
IP address is a 32-bit number assigned to each network interface of a node.
Nodes (such as routers) with multiple network interfaces have multiple IP addresses.
IP Address in Dotted-Decimal Notation
3

## Slide 4: Network Prefix; Host Portion
4
An IP address has two components
  Network prefix
    Identifying a link
    Identical for all nodes attached to the same link
  Host portion
    Identifying a specific host or router connected to that link
Example: 129.61.18.26, prefix length = 24
  Network prefix = 129.61.18
  Host portion = 26

## Slide 5: Routing Table
5
Router A Router B
Router C
Host 1
Target / Prefix- Length | Next Hop | Interface
7.7.7.99 / 32 | router 1 | a
7.7.7.0 / 24 | router 2 | a
0.0.0.0 / 0 | router 3 | a
Host 1’s routing table
a
Host 1 wants to forward a packet to 7.7.7.1
Rules for Routing:
Compare the left-most Prefix-Length bits of each Target with the IP destination address.
Choose the matching route with the largest Prefix-Length.
Default route

## Slide 6: A Routing Example: 1.0.0.1  2.0.0.4
1.0.0.1
1.0.0.2
1.0.0.254
3.0.0.254
a
a
a
c
3.0.0.252
3.0.0.253 c
b
2.0.0.3 2.0.0.4
2.0.0.253
b
b
c
b b
Host 1
Host 2
Host 5
Router A
Router C
Target/Prefix-Length | Next Hop | Interface
1.0.0.0 / 24 | “direct” | a
0.0.0.0 / 0 | 1.0.0.254 | a
Host 1’s routing table
Ethernet A Network Prefix = 1.0.0
High-Speed Fiber Backbone Network Prefix = 3.0.0
Router B
Ethernet B Network Prefix = 2.0.0
Host 3 Host 4
4.0.0.5
4.0.0.252
Ethernet C Network Prefix = 4.0.0
6

## Slide 7: A Routing Example: 1.0.0.1  2.0.0.4
1.0.0.1
1.0.0.2
3.0.0.254
a
a
a
c
3.0.0.252
3.0.0.253 c
b
2.0.0.3 2.0.0.4
2.0.0.253
4.0.0.5
b
b
b
c
b
Host 1
Host 2
Host 5
Router A
Router C
Target/Prefix-Length | Next Hop | Interface
1.0.0.0 / 24 | “direct” | a
3.0.0.0 / 24 | “direct” | c
2.0.0.0 / 24 | 3.0.0.253 | c
4.0.0.0 / 24 | 3.0.0.252 | c
1.0.0.254
Router A’s routing table
Ethernet A Network Prefix = 1.0.0
High-Speed Fiber Backbone Network Prefix = 3.0.0
Router B
Ethernet B Network Prefix = 2.0.0
Host 3 Host 4
4.0.0.252
Ethernet C Network Prefix = 4.0.0
7

## Slide 8: A Routing Example: 1.0.0.1  2.0.0.4
1.0.0.1
1.0.0.2
3.0.0.254
a
a
a
c
3.0.0.252
3.0.0.253 c
b
2.0.0.3 2.0.0.4
2.0.0.253
4.0.0.5
b
b
b
c
b
Host 1
Host 2
Host 5
Router A
Router C
Target/Prefix-Length | Next Hop | Interface
1.0.0.0 / 24 | 3.0.0.254 | c
2.0.0.0 / 24 | “direct” | b
3.0.0.0 / 24 | “direct” | c
1.0.0.254
Router B’s routing table
Ethernet A Network Prefix = 1.0.0
High-Speed Fiber Backbone Network Prefix = 3.0.0
Router B
Ethernet B Network Prefix = 2.0.0
Host 3 Host 4
4.0.0.252
Ethernet C Network Prefix = 4.0.0
8

## Slide 9: A Routing Example: 1.0.0.1  2.0.0.4
1.0.0.1
1.0.0.2
3.0.0.254
a
a
a
c
3.0.0.252
3.0.0.253 c
2.0.0.3
2.0.0.253
2.0.0.4
4.0.0.5
4.0.0.252
b
b
c
b b
Host 1
Host 2
Host 4
Host 5
Router A
Router C
Target/Prefix-Length | Next Hop | Interface
1.0.0.0 / 24 | 3.0.0.254 | c
2.0.0.0 / 24 | “direct” | b
3.0.0.0 / 24 | “direct” | c
1.0.0.254
Router B’s routing table
Ethernet A Network Prefix = 1.0.0
High-Speed Fiber Backbone Network Prefix = 3.0.0
Router B
Ethernet B Network Prefix = 2.0.0
Host 3
Ethernet C Network Prefix = 4.0.0
?
b

## Slide 10: Problem
The packet is undeliverable
– Host 4 is not connected to Ethernet B.
Router B will then send a Host Unreachable
error message back to Host 1.
Q: How to solve it?

## Slide 11: Solution 1: Host-Specific Route
Place host-specific routes in the routing tables of Router A, B, and C as follows:
Target/Prefix-Length | Next Hop | Interface
2.0.0.4 / 32 | 3.0.0.252 | c
Target/Prefix-Length | Next Hop | Interface
2.0.0.4 / 32 | 3.0.0.252 | c
Target/Prefix-Length | Next Hop | Interface
2.0.0.4 / 32 | “direct” | b
Router A
Router B
Router C
Is this a good solution?

## Slide 12: Solution 2: Change IP Address
Simply change the IP address of host 4, as it moves from Ethernet B to Ethernet C.
For example, Dynamic Host Configuration Protocol (DHCP) can be used to acquire a new IP address.
Q: Is this a good solution?

## Slide 13: Solution 3: Mobile IP
A standard proposed to solve the problem of Internet mobility.
It allows the mobile node to use two IP addresses:
  a fixed home address
  a care-of address that changes at each new point of attachment

## Slide 14: Entities and Relationships
Home Link – the link having the same network prefix as the node’s IP address
Mobile Node “at home”
Home Agent – a router on the mobile node’s home link.
Foreign Agent
Foreign Agent
Foreign Link
Foreign Link
Mobile Node
“visiting” a foreign link

## Slide 15: Care-of Address
Two conceptual types of care-of addresses
  Foreign agent care-of address
  Collocated care-of address

## Slide 16: Foreign Agent Care-of Address
IP address of a foreign agent which has an interface on the foreign link.
– The foreign agent may have more than one IP address; hence, the network-prefix need not equal the network prefix of the foreign link
The same address can be shared by many mobile nodes simultaneously.

## Slide 17: Collocated Care-of Address
An IP address temporarily assigned to a mobile node.
– It can be used by only one mobile node at a time.
The network prefix must equal the network prefix of the foreign link.
It might be used by a mobile node in situations where no foreign agents are available.

## Slide 18: Three Mechanisms
Agent Discovery
Registration
Routing

## Slide 19: 1. Agent Discovery
Home Agents and Foreign Agents periodically broadcasts Agent Advertisements.
  e.g. once every few seconds
  If the mobile node does not want to wait for the periodic advertisement, it can broadcast Agent Solicitations that will be answered by any foreign agent that receives it.
Mobile nodes determine whether they have moved from one link to another. (How?)

## Slide 20: Move Detection
Agent Advertisement has a Lifetime field.
– specify how soon a mobile node should expect to hear another advertisement from that same agent.
If the mobile node fails to hear an advertisement from that agent within the specified Lifetime, then it assumes that it has moved to a different link.

## Slide 21: Care-of Address
A mobile node connected to a foreign link acquire a foreign agent care-of-address from the Agent Advertisements.
– If multiple care-of-addresses are listed, any one of them can be used.
If a foreign agent is unavailable, the mobile node obtain a collocated care-of address by Dynamic Host Configuration Protocol (DHCP).

## Slide 22: DHCP
Goal
– allow host to dynamically obtain its IP address from network server when it joins a network
A client-server protocol
Four-way handshake

## Slide 23: DHCP Client-Server Scenario
223.1.1.1
223.1.1.3
223.1.1.2
223.1.1.4 223.1.2.9
223.1.2.1
223.1.3.1
223.1.3.27
223.1.2.2 E
223.1.3.2
DHCP
server
arriving DHCP client needs address in this network
DHCP relay agent (typically a router) for
223.1.1 and 223.1.3.
It knows the address of a DHCP server for these networks.

## Slide 24: Broadcast arriving Address:
DHCP server: 223.1.2.5
time
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
Lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
Lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
Lifetime: 3600 secs
Choose an offer if more than one server replies.
client 255.255.255.255
UDP port 67
What is source address?
Allocates an IP address and set the time for which the address will be valid.

## Slide 25: 2. Registration
Registration is the process by which a mobile node
  requests routing services from a foreign agent;
  informs its home agent of its current care-of address;
  renews a registration which is due to expire;
  deregisters when it returns to its home link.

## Slide 26: Scenario 1: Registering Foreign Agent Care-of Address
Foreign Agent
Home Agent
1
2
3
4
The mobile node, with the assistance of a foreign agent, sends a Registration Request with the care-of address information.
When the home agent receives this request, it adds the necessary information to its routing table, and sends a Registration Reply back to the mobile node.
Mobile Node “visiting” a foreign link

## Slide 27: Scenario 2: Registering Collocated Care-of Address
Registration Request
Mobile Node “visiting” a foreign link
Home Agent
Registration Reply

## Slide 28: Scenario 3: Deregistration
1. (de-)Registration Request
Mobile Node returns to its home link
Home Agent
2. (de-)Registration Reply

## Slide 29: Authentication
The home agent must be certain that registration was originated by the mobile node and not by some other malicious node.
Registration of the care-of address requires authentication.
  The mobile node needs to prove its identity to its home agent.
  It is done by making use of a secret key known only to the mobile node and its home agent.

## Slide 30: 3. Routing
Different Scenarios:
Mobile Node → Correspondent Node
Correspondent Node → Mobile Node
  With a foreign agent
  Without a foreign agent

## Slide 31: How to Send Packets to a Correspondent Node?
Foreign Agent
Home Agent
Correspondent
Mobile Node
Simply use the Correspondent’s IP address as the destination address.
How about the source address? Original IP address? Care-of Address?

## Slide 32: How to Send Packets to a Mobile Node?
Foreign Agent
Home Agent
Correspondent
Mobile Node
Source address | Correspondent’s IP address
Destination address | Mobile’s IP address

## Slide 33: Tunneling to the Care-of Address
Foreign Agent
Home Agent
Mobile Node “visiting” a foreign link
Tunnel
Home Agent intercepts packets destined to the mobile node’s home address and tunnels them to the mobile node’s care-of address.
Foreign Agent removes original packet from the tunnel and delivers the original packet to the mobile node over the foreign link.

## Slide 34: IP in IP Encapsulation
Header
Payload
Original IP packet
Ipsrc = Original Sender
Ipdes = Destination’s Home Address
Outer Header
Outer Payload
Encapsulating IP packet
Header
Payload
The home agent inserts a new IP header, or tunnel header, in front of the IP header of any datagram addressed to the mobile node’s home address.
Ipsrc = Home Agent
Ipdes = Mobile node’s Care-of Address

## Slide 35: Triangle Routing
Mobile Node “visiting” a foreign link
Foreign Agent
Home Agent
Correspondent
Why doesn’t the mobile node inform the correspondent of its care-of address and have it tunnel directly to the mobile node?

## Slide 36: Optimized Routing
Mobile Node “visiting” a foreign link
Foreign Agent
Home Agent
Correspondent
This is potentially more efficient in terms of delay and resource consumption.
Why is it not used?

## Slide 37: Main Obstacle: Security
Mobile Node “visiting” a foreign link
Foreign Agent
Home Agent
Correspondent
A bad guy sends a fake registration to the correspondent
It is impractical to distribute keys between a mobile node and every other node with which it might correspond.

## Slide 38: References
J. D. Solomon, Mobile IP: the Internet unplugged, Prentice Hall, 1998.
C. E. Perkins, “Mobile networking through mobile IP,”
IEEE Internet Computing, pp. 58-69, Jan/Feb, 1998.